## Slide 1: CNN projects for Spring 2015

## Slide 2: Members
"Jayaprakash, Sangeetha" sjayaprakash6@gatech.edu
Joshua Lee jlee755@gatech.edu
Ria Gupte ria.gupte@gmail.com
"Diao, Enmao" <emdiao@gatech.edu>

## Slide 3: 2 1 Groups
FPGA implementation group
  step1 : Write a simple CNN using matlab or C source code
  step 2: Naïve CNN on FPGA
  step 3: KAIST_CNN on FPGA
  step 4: SP_CNN on FPGA
  step 5: Bigger scales on FPGA
CNN algorithm developments
  Functional simulator
  Test out other inputs
  Other neural networks
  Convolutional neuron network
future work

## Slide 4: CNN Simulator
https://dmanatunga@bitbucket.org/dmanatunga/cnn-simulator.git
author: Dilan Manatunga manatunga@gmail.com
Look at matlab directory, look at the holefiling example

## Slide 5: Naïve CNN
C(I,j)
C(I,j)
8-bit operations
input comes from a memory
Registers for A,B templates
y function is fixed
Put a ALU for functional units

## Slide 6: First CNN Design
6x6 CNN
input image 8 bits. (6x6 image cells)
MAC: Multiply + Adder
Each cell has 9 MAC units to compute with outputs, 9 MAC units to compute with neighbor input values, 1 final adder to sum constant
A,B, I value registers

## Slide 7: MAC Sharing CNN
Naïve CNN: All 9 inputs are summed together
MAC sharing CNN: use only 1 MAC unit to sum all 9 inputs
 A basic model for KAIST_CNN

## Slide 8: KAIST_CNN
ALUs are shared
Required a shift register

## Slide 9: SP-CNN
Start from CNN-P ,
Connect with a SRAM memory
2 CNN-Ps
Connect with a SRAM memory